## Slide 1: Electricity Generation, Transmission and Distribution: what does the future hold?
Bryan Leyland, MSc, FIEE(rtd), FIMechE, FIPENZ. Leyland Consultants

## Slide 2: Generation
Future options are:
  fossil fuels
  nuclear
  hydro
  new renewables
    wind solar, tidal, wave etc

## Slide 3: Fossil fuels
Every year peak oil moves further into the future
Shale gas has transformed the industry
The clathrate (methane ice) resource is immense
There are huge resources of coal
  clean coal stations emit CO2 and water
    CO2 enhances plant growth and benefits agriculture

## Slide 4
Fossil fuel resource is huge!

## Slide 5: Nuclear Energy
Uranium resources
  proven:~80 years supply
  expected:~250 years supply
    1000+ years with breeder reactors!
Energy from thorium
  3 times as abundant as uranium >750 years supply
Nuclear power could supply all the energy we need for more than 500 years

## Slide 6
Safe
Dangerous
Fatal
Death
rates
Regulated
levels are
~1 mSv
2000 mSv
is safe!

## Slide 7: Hydro, Geothermal and Renewables
Hydro and Geothermal
  will continue to provide power when it is needed at low cost
Wind and Solar
  intermittent and expensive
  impose high costs on the system
    backup and transmission
Tidal, Wave etc
  nowhere near commercial viability
  SeaWave may succeed
    and make all other wave power devices obsolete overnight

## Slide 8: Transmission in New Zealand
Several years ago it was suggested that one pole of the DC link should be extended to Auckland
  if it had gone ahead, the $900 million 400 kV line would not have been needed
15 years ago the then CEO of Transpower decided that distributed generation was going to make transmission systems obsolete
  it didn’t happen and the catchup was difficult and expensive
In many countries distributed generation in the form of subsidised solar and wind power is progressing rapidly
  this requires lot of new transmission
    we can conclude that distributed generation needs even more transmission!

## Slide 9: DC transmission
Advantages of DC for point to point transmission
  two conductors instead of three
  no skin effect – lower losses, higher current and larger conductors
  no reactive power problems
  asynchronous connection
Disadvantages are:
  high cost of terminal equipment
  problems with multi terminal systems

## Slide 10: Future of DC transmission
The cost of terminal equipment is steadily decreasing
The cost of underground DC cables is steadily decreasing
DC circuit breakers are now available
DC will supersede AC for long-distance extra high voltage transmission
  Will the 400 kV AC line become part of a 500 kV DC network?

## Slide 11: Distribution
The technology has barely changed in the last 100 years
  medium voltage transmission and low voltage distribution have served us well
  in the long term, DC and power electronics may take over.
The most pressing problem is with the US-based 110 V system that needs a distribution transformer for every 4 to 6 houses
  should it change to say, 660/400 V with a transformer in each house to supply low power loads?
  Or should it change to DC?
A major part of household load is electronic equipment with AC to DC converters
  Should every house have an AC to DC system?
    300 V for major loads and 24 V for minor loads?

## Slide 12: Solar power
Solar power is intermittent and 3 to 5 times more expensive than conventional
A mistaken belief that solar power will substantially reduce carbon dioxide emissions has led to very large subsidies
    e.g. $1000/kW plus high prices for feedback even when the system does not need it
Many people are installing solar cells
This can cause major problems for the distribution system
  voltage problems in the middle of the day
  distribution system must supply the total load when the sun is not shining
The cost of the subsidies and system reinforcement is imposed on all consumers
  so there is a transfer of wealth from poor consumers to those who can afford solar panels
    I believe that this is disgraceful in the extreme
If the subsidies were abandoned, the industry would die
  roll on the day!

## Slide 13: Electric cars
Attract government grants, subsidies and other benefits based on small and expensive CO2 reduction
  Sales have been disappointing
    for 2015, 1 million predicted, 300,000 actual (USA)
    55% of electric cars replaced with a conventional one
  Electricity demand could be a problem
    in the USA, many distribution transformers could be overloaded
It is claimed that electric car batteries could be used for energy storage
  But the cost is excessive – about 30 cents for every kWh stored
Another expensive and ineffective technology aimed at solving a problem that does not exist!

## Slide 14: Smart grids
Nothing new: grids have always been smart
  new and expensive smart technologies could be needed to manage the integration of wind and solar power
    better still abandon these expensive and unreliable technologies
Smart metering
  huge sums have been spent on smart metering because governments have been persuaded that it benefits the consumer, reduces peak demands and reduces CO2
    failed on all three counts
      the costs exceed the benefits
  Small savings in meter reading costs –~ $1 per meter read
  A major factor in the rundown of our once world leading ripple control system
    we control peak demands less than before
      a giant step backwards

## Slide 15: No relationship between price and demand

## Slide 16: What ripple control can – and could – do.

## Slide 17: What does the future hold?
Wind and solar power
  $2 trillion has brought a very small return in CO2 reduction
    in a world that has not warmed for 18 years.
  Renewable energy subsidies have increased the cost of power to poor people
  Unpredictable output brings the risk of serious power shortages
  A rational society would abandon it
Fossil fuels
  can provide a low cost reliable supply for the foreseeable future
Nuclear energy
  Most people believe it is dangerous
    in fact it is very safe
    low levels of radiation are NOT dangerous
  Can provide all the energy we need reliably and at low cost
    needs a major change in attitude by the industry and regulators

## Slide 18: What does the future hold?
DC transmission
  will advance steadily and, maybe, supersede EHV AC
Distribution systems
  will continue without much change unless
    subsidies continue for uneconomic domestic solar power
    electric car subsidies continue and batteries improve substantially
Smart metering
  will continue in spite of of dubious economics
  will fail to make a substantial contribution to demand side management

## Slide 19: My predictions
In 25 years time:
  dangerous man-made global warming will be forgotten
  the world will be using even more fossil fuels
  mining for clathrates will be well underway
  nuclear power will be expanding
  dismantling wind and solar installations will be an expensive problem
  integrated high-voltage DC networks will be emerging
  distribution systems will be much the same as they are now
  electric cars will be less than 25% of the fleet
  the more exotic aspects of smart grids will be forgotten
  smart metering will continue to fail to deliver on expectations